Abstract DC Drive CAN message formatting
IDB – broadcast ID
ID – Individual ID
offset – unique number for each drive in CAN. Set in can.c.
By default used not extended ID.
# Setting the PID parameters (IDB = 200, ID = 200 + offset)

47	46	45	44	43	42	41	40	39	38	37	36	35	34	33	32
TYPE [31:24]								FIELD[23:16]

31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16
VALUE[31:16]

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
VALUE[15:0]

Bits 47:40 TYPE Type of PID that is being configured
0000 0001: Speed PID
0000 0011: Current PID
0000 0100: Position PID

Bits 39:32 FIELD Field of PID that is being configured
0000 0000: Proportional coefficient
0000 0001: Integral coefficient
0000 0011: Differential coefficient
0000 0100: Coefficient on which will be divided all coefficients. Must not be 0
0000 0101: Number of measurement that is used to find average value and than used as feedback data (used only in the current PID)

Bits 31:0 VALUE Value to be set (int32_t)
# Save settings of a PID to FLASH (IDB = 200, ID = 200 + offset)

7	6	5	4	3	2	1	0
TYPE [7:0]

Bits 7:0 TYPE Type of PID which settings should to be set
0000 0001: Speed PID
0000 0011: Current PID
0000 0100: Position PID
# Setting desired value of PID (IDB = 100, ID = 100 + offset)

39	38	37	36	35	34	33	32
TYPE [39:32]

31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16
VALUE[31:16]

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
VALUE[15:0]

Bits 39:32 TYPE Type of PID desired value of which should be set. This also switch PID mode of the drive to this type.
0000 0000: None (apply 0 voltage)
0000 0001: Speed PID
0000 0011: Current PID
0000 0100: Position PID
0000 0101: Direct control

Bits 31:0 VALUE Value to be set (int32_t)
# 3. Request a LOG (IDB = 900, ID = 900 + offset)

7	6	5	4	3	2	1	0
TYPE [7:0]

Bits 7:0 TYPE Type of LOG that should be requested.
0000 0001: Speed
0000 0011: Current
0000 0100: Position
0000 0101: Voltage

# LOG response
Speed log ID = 1024 + offset
Postion log ID = 1152 + offset
Current log ID = 1280 + offset
Temperature log ID = 1536 + offset
Voltage log ID = 1664 + offset

31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16
VALUE[31:16]

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
VALUE[15:0]

Bits 31:0 VALUE Value of a response (int32_t)